## Slide 1: Spectral Global Intrinsic Symmetry Invariant Functions
Hui Wang
Shijiazhuang Tiedao University
Patricio Simari The Catholic University of America
Zhixun Su
Dalian University
of Technology
Hao Zhang
Simon Fraser University

## Slide 2: Introduction
Global Intrinsic Symmetry Invariant Functions (GISIFs) are functions defined on a manifold invariant under all global intrinsic symmetries
Useful in shape analysis:
  Critical points of GISIFs obtained via geodesic distances form symmetry invariant point sets for the generation of candidate Mobius transformations
  Classical Heat Kernel Signature (HKS) Wave Kernel Signature (WKS) – both GISIFs -- are used as symmetry invariant descriptors for correspondence

## Slide 3: Introduction
We propose a new class of GISIFs over compact Riemannian manifolds
Spectral method: each eigenvalue of the Laplace-Beltrami operator, either repeated or non-repeated, corresponds to a GISIF.

## Slide 4: Main Related Work
M. Ovsjanikov, J. Sun, and L. Guibas. “Global intrinsic symmetries of shapes”. Computer Graphics Forum, 27(5):1341–1348, 2008.
V. G. Kim, Y. Lipman, and X. Chen. “Möbius transformations for global intrinsic symmetry analysis”. Computer Graphics Forum, 29(5):1689–1700, 2010.
Y. Lipman, X. Chen, I. Daubechies, and T. A. Funkhouser. “Symmetry factored embedding and distance”. ACM Transactions on Graphics, 29(4):439–464, 2010.

## Slide 5: Background
A global intrinsic symmetry on a particular manifold is a geodesic distance-preserving self-homeomorphism.
T: M  M is a global intrinsic symmetry if for all p, q in M it holds that where g denotes geodesic distance

## Slide 6: Background
A global intrinsic symmetry invariant function (GISIF) is any function f: M  R such that for any global intrinsic symmetry T it holds that f o T = f.
In other words, if for all p in M it holds that

## Slide 7: Background
Some useful propositions:
  Constant functions, f(p) = c for all p, are GISIFs
  If f is a GISIF then c * f is a GISIF
  If f and g are GISIFs, then f + g, g – f, f * g, and f/g (for g ≠ 0) are all GISIFs
Based on the above propositions, all of the GISIFs defined on a manifold form a linear space called the global intrinsic symmetry invariant function space.

## Slide 8: Spectral GISIFs via the LB Operator
We propose a new class of GISIFs based on the eigendecomposition of the Laplace-Beltrami operator on compact Riemannian manifolds without boundaries.
Each GISIF corresponds to an eigenvalue, repeated or non-repeated, of the Laplace-Beltrami operator.
Formally stated…

## Slide 9: Spectral GISIFs via the LB Operator
Theorem: Suppose M is a compact Riemannian manifold without boundary, λi is an eigenvalue of the Laplace-Beltrami operator Δ on M with a k-dimensional eigenfunction space. If φi1, φi2, …, φik is an orthogonal basis of the corresponding eigenfunction space of λi, then the function is a GISIF on M.
Discretized on meshes and point clouds (cotangent weights).
Generalizes HKS, WKS, ADF…

## Slide 10: Results
fi_j denotes a GISIF computed using eigenfunctions of the Laplace-Beltrami operator corresponding to repeated eigenvalues i through j
Less “detail”
More “detail”

## Slide 11: Results
fi_j denotes a GISIF computed using eigenfunctions of the Laplace-Beltrami operator corresponding to repeated eigenvalues i through j

## Slide 12: Results
fi_j denotes a GISIF computed using eigenfunctions of the Laplace-Beltrami operator corresponding to repeated eigenvalues i through j

## Slide 13: Results: Sparsity
Level sets and histograms of our spectral GISIFs. The large blue areas without contours along with the histograms of each field illustrate the sparsity of the fields.

## Slide 14: Results: Sparsity
Level sets of our spectral GISIFs. The large blue areas without contours along with the histograms of each field illustrate the sparsity of the fields.

## Slide 15: Results: Robustness to Noise
Original
Gaussian Noise: 20% mean edge length

## Slide 16: Results: Comparison to HKS
Some of our spectral GISIFs
HKS for varying times (default parameters)

## Slide 17: Results: Comparison to AGD
Some of our spectral GISIFs
AGD
Topological noise

## Slide 18: Applications: SFDs
Symmetry Factored Embedding (SFE):
Symmetry Factored Distance (SFD):
The SFDs between a point and its symmetric points are zero.

## Slide 19: Applications: SFDs
Symmetry-factored distances (SFDs) computed using spectral GISIFs from the red points shown. Note how the SFDs between each point and its symmetric points are near zero (blue).

## Slide 20: Applications: SFDs
Symmetry-factored distances from the red points
Symmetry orbits from the red points

## Slide 21: Applications: SFDs
Symmetry-factored distances from the red points
Symmetry orbits from the red points
Symmetry-factored distances from the red points
Symmetry orbits from the red points

## Slide 22: Application: Segmentation
Symmetry-aware segmentations: k-means clustering on the SFE -- preliminary result

## Slide 23: Summary and Limitations
Propose a new class of GISIFs: Spectral GISIFs
  More robust to topological noise than those based on geodesic distances
  Generalizes HKS, WKS, ADF…
Presented applications:
  Symmetry orbits
  symmetry-aware segmentations (preliminary)
Limitations:
  Cannot be computed on non-manifold shapes
  Difficult for a user to decide which spectral GISIFs to use out of the full spectrum and if/how to combine them

## Slide 24: Future Work
Theory:
  Study relation between global intrinsic symmetry and multiplicity of eigenvalues of the LB operator
  Formal derivation of sparsity property
Heuristics:
  Choosing of most informative GISIFs (e.g., entropy)
  Setting threshold for detecting repeated eigenvalue
Symmetry-aware applications:
  skeletonization
  texture synthesis
  denoising,
  repair
  processing and analysis of high-dimensional manifolds

## Slide 25: Thank You!